## Slide 1
Final presentation Customization of RISCV code and backend design of a RISCV processor - 7880
By: Omar Sharafy, Muhammad Biadsy
Instructor: Amnon Stanislavsky
VLSI Lab
Winter & spring Semesters 2024/25

## Slide 2: Agenda
Background.
Project definition and goals.
Alternative solutions.
Architectural design of the selected solution.
Back-end flow.
Results

## Slide 3: Background & Motivation
RISC-V is a simple architecture which is being taught in “digital systems & computer structure”.
The purpose of this project is to take the pipelined version of RISC V presented in the course and prepare it for a potential fabrication, while:
1) making other changes that will reduce the required area & power memories consume (by using Tower SRAMs).
2) create an external memory loading method.
3) adding debugging capabilities that allow access to internal registers. after fabrication.
The original code needs to be modified to allow the backend stages to be executed correctly.

## Slide 4: Goals
Replacing
Replacing non-synthesizable memory-loading techniques with an external interface.
Upgrading
Upgrading inefficient course-provided memories to compact, compiled memories, which are more power and size effective.
Adding
Adding debug capabilities for accessing internal registers post-fabrication.
Performing
Performing a back-end physical design flow, while optimizing frequency by refining Verilog code.

## Slide 5: Alternative solutions
the RISC-V Processor that we work with can utilize FPGA memories and the control unit as a debug tool to monitor internal signals, while leveraging the initial lines of code to load the desired memory into the compiled memory.
Although this solution is possible, FPGA memories are not effective size or power wise.

## Slide 6: Architectural design of the selected solution memory replacement

## Slide 7: Architectural design
Using SRAM memories, which are area & power efficient, allowing simultaneous read and write operations to multiple addresses.
Create a dedicated debugging unit, separate from the control unit. to provide additional debugging capabilities.
Add 2 input pins, creating a memory loading flow.

## Slide 8: Architectural design of the selected solution memory loading mechanism
adding 2 input pins (one for data, one for instructions), and taking advantage of the fact that Tower S-RAMs can write to 2 different addresses in parallel.

## Slide 9: Architectural design of the selected solution Debug unit
حط جدول الכניסות וחיבורים
احكي عن الموكس
ليش أصلا رجعنا للموكس

## Slide 10: Back-end flow:
Using Synopsys Design Vision tool & TSMC TSL 108 Tower Design Kit for Synthesis flow, converting the RTL design into a gate-level netlist that matches the target manufacturing process.
Using Cadence Innovus tool & TSMC TSL 108 Tower Design Kit for a short layout flow, transforming a synthesized Verilog design into a complete physical chip layout, while trying to maximize the working frequency.
Using PrimeTime Tool to verify and debug timing issues, to reach maximum working frequency.

## Slide 11: Challenges & problems
Design Size was getting a lot bigger due to the initial debug unit planning, creating a high-density & complex design.
-We had to re-plan, and used a common solution used in the real world, adding a mux to the debug unit outputs, reducing the design size by ~ %60.
Inconsistencies between tools used in different back-end manuals, This limitation was shown during our attempt to use PrimeTime (as guided in the long manual) within a project originally structured using the short manual, causing us to create a new script ( with Goel help).

## Slide 12: Results
Maintained Risc-v operations.
Added support for full memory space access in memory operations (previously, only addresses divisible by 4 were supported).
A Clock Tree with 1.3ns slack.
166.67 MHz working frequency.
Add a critical memory path ( both here and in report)